## Slide 1: P&S Modern SSDs Advanced NAND Flash Commands & Address Translation
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Spring 2022
4 April 2022

## Slide 2: Recap: SSD & NAND Flash Memory
SSD organization
  SSD controller: Multicore CPU + per-channel flash controllers
  DRAM: Metadata store, 0.1% of SSD capacity
  NAND flash chips
    Channel (Package(s)) – Die (Chip) – Plane – Block – Page
NAND flash characteristics
  Erase-before-write, asymmetry in operation units (read/program: page, erase: block), limited endurance, retention loss…
Basic NAND flash opeartions
  Read/program/erase

## Slide 3: Today’s Agenda
Advanced NAND Flash Commands
Address Translation & Garbage Collection
Advanced NAND Flash Commands
Address Translation & Garbage Collection

## Slide 4: SSD Performance
Latency (or response time)
  The time delay until the request is returned
  Average read latency (4 KiB): 67 us
  Average write latency (4 KiB): 47 us
Throughput
  The number of requests that can be serviced per unit time
    IOPS: Input/output Operations Per Second
  Random read throughput: up to 500K IOPS
  Random write throughput: up to 480K IOPS
Bandwidth
  The amount of data that can be accessed per unit time
  Sequential read bandwidth: up to 3,500 MB/s
  Sequential write bandwidth: up to 3,000 MB/s
HDD:
~100 MB/s
HDD:
> 1K IOPS
HDD:
5~8 ms
Source: https://www.anandtech.com/show/16504/the-samsung-ssd-980-500gb-1tb-review

## Slide 5: NAND Flash Chip Performance
Chip operation latency
  tR: Latency of reading (sensing) data from the cells into the on-chip page buffer
  tPROG: Latency of programming the cells with data in the page buffer
  tBERS: Latency of erasing the cells (block)
  Varies depending on the MLC technology, processing node, and microarchitecture
    In 3D TLC NAND flash, tR/tPROG/tBERS ≈ 100us/700us/3ms
I/O rate
  Number of bits transferred via a single I/O pin per unit time
  A typical flash chip transfers data in a byte granularity (i.e., via 8 I/O pins)
  e.g., 1-Gb I/O rate & 16-KiB page size  tDMA = 16 us

## Slide 6: NAND Flash Chip Performance (Cont.)
tR, tPROG, and tBERS
  Latencies for chip-level read/program/erase operations
  tR: 50~100 us
  tPROG: 700us~1000 us
  tBERS: 3ms~5ms
Flash-controller level latency
  1-Gb I/O rate and 16-KiB page size
  Read
    (tCMD) + tR + tDMA + tECCDEC + (tRND)
    e.g., 100 + 16 + 20 = 136 us
NAND Flash Chip
Flash Controller
RAND
ECC
READ(x)
❷ Sensing
❸ Transfer
❹
❺
❶

## Slide 7: NAND Flash Chip Performance (Cont.)
tR, tPROG, and tBERS
  Latencies for chip-level read/program/erase operations
  tR: 50~100 us
  tPROG: 700us~1000 us
  tBERS: 3ms~5ms
Flash-controller level latency
  1-Gb I/O rate and 16-KiB page size
  Read
    (tCMD) + tR + tDMA + tECCDEC + (tRND)
    e.g., 100 + 16 + 20 = 136 us
  Program
    (tRND) + tECCENC + (tCMD) + tDMA + tPROG
    e.g., 20 + 16 + 700 = 736 us
NAND Flash Chip
Flash Controller
RAND
ECC
WRITE(x)
❺ Program
❹ Transfer
❶
❷
❸

## Slide 8: NAND Flash Chip Performance (Cont.)
How about bandwidth?
  Read
    16 KiB / 136 us ≈ 120 MB/s
  Write
    16 KiB / 736 us ≈ 22 MB/s
WAIT!
SSD read latency: 67 us
SSD read bandwidth: 3.5 GB/s
SSD write latency: 47 us
SSD write bandwidth: 3 GB/s
Optimizations w/ advanced commands
DRAM/SLC Write Buffer
NAND Flash Chip
Flash Controller
RAND
ECC
NAND Flash Chip
Flash Controller
RAND
ECC
NAND Flash Chip
Flash Controller
RAND
ECC
Internal parallelism
…

## Slide 9: Advanced Commands for Small Reads
Minimum I/O units in modern file systems: 4 KiB
  Latency & bandwidth waste due to I/O-unit mismatch
  e.g., A page read unnecessarily reads/transfers 12-KiB data
Optimization 1: Sub-page sensing
  e.g., Micron SNAP READ operation1
  Microarchitecure-level optimization – directly reduces tR
Optimization 2: Random Data Out (RDO)
  Data transfer with an arbitrary offset and size
  Reduce tDMA and tECCDEC
1https://media-www.micron.com/-/media/client/global/documents/products/technical-note/nand-flash/tn_2993_snap_read.pdf

## Slide 10: CACHE READ Command
Performs consecutive reads in a pipelined manner
tECC
READ A
READ B
PAGE READ
Regular PAGE READ:
Overlaps only tECC with tR
READ A
READ B
CACHE READ
CACHE READ:
Overlaps tDMA & tECC with tR
tDMA
tR

## Slide 11: Enabling the CACHE READ Command
Needs additional on-chip page buffer
READ A
READ B
CACHE READ
NAND Flash Plane
Page A
Page B
…
Page A
❶ PAGE READ(A)
PAGE READ
Page Buffer 1
Page Buffer 2
❸ CACHE READ(B)
❷ Page senging
❹ Page senging
❺ DATA OUT(A)
(Toggle RE signal)

## Slide 12: CACHE READ Command: Benefit
Removes tDMA from the critical path
  Increases throughput/bandwidth
  Reduces effective latency
    By reducing the time delay for a request being blocked by the previous request

## Slide 13: Multi-Plane Operations
Concurrent operations on different planes
  Recall: Planes share WLs and row/column decoders
Opportunity: Planes can concurrently operate
Constraints: Only for the same operations on the same page offset
Plane0
Plane1
Plane2
Plane3
Page Buffers
Peripheral Circuits
Row/Column Decoders
WL k
VREF
WL x
VPASS
(others)
Taget Page
Same voltage can be
applied to all cells

## Slide 14: Multi-Plane Operations: Benefit
Increase the throughput/bandwidth almost linearly with # of planes that concurrently operate
  Bandwidth with regular page programs: 16 KiB / 736 us ≈ 22 MB/s
  Bandwidth with multi-plane page programs (2 plane): 32 KiB / 736 + 16 (tDMA) + 20 (tECC) us ≈ 41.5 MB/s
Per-operation latency increases
  Regular page program: tECCENC + tDMA + tPROG
  Multi-plane page program: NPlane×(tECCENC + tDMA) + tPROG
The benefits highly depend on the access pattern and FTL’s data placement
  Random-read-dominant vs. Random-write-dominant

## Slide 15: Program & Erase Suspensions
Read performance is often more important
  Writes can be done in an asynchronous manner using buffers
    e.g., return a write request immediately after receiving the data (and storing it to the write buffer)
  A read request can be returned only when the requested data is ready (after reading the data from the chip)
Significant latency asymmetry
  tR: 100 us, tPROG: 700 us, tBERS: 5 ms (TLC NAND flash)
    If the chip is designed to program all the pages in the same WL at once, the actual program latency is 2,100 us
  The worst-case chip-level read latency can be 50x longer than the best-case latency

## Slide 16: Program & Erase Suspensions (Cont.)
Suspends an on-going program (erase) operation once a read arrives
  Pros: Significantly decreases the read latency
  Cons
    Additional page buffer (for data to program)
    Complicated I/O scheduling (Until when can we suspend on-going program requests?)
    Negative impact on the endurance
R
100 us: Read arrival
Latency: 700 us
Latency: 700 us
P
R
100 us: Read arrival
Latency: ~100 us
Latency: ~800 us
P
P
Suspend

## Slide 17: Summary
Subpage Sensing & Random Data Out (RDO)
  For I/O-unit mismatch b/w OS and NAND flash memory
Cache Read Command
  For improving a chip’s read throughput
  By overlapping data transfer and page sensing
Multi-Plane Operations
  For improving a chip’s throughput
  By enabling concurrently operation of multiple planes
Program & Erase Suspensions
  For improving the read latency (operation latency asymmetry)
  By prioritizing latency-sensitive reads over writes/erases

## Slide 18: Today’s Agenda
Advanced NAND Flash Commands
Address Translation & Garbage Collection

## Slide 19: Flash Translation Layer: Overview
SSD firmware (often referred to as SSD controller)
  Provides backward compatibility with traditional HDDs
  By hiding unique characteristics of NAND flash memory
Responsible for many important SSD-management tasks
  Address translation + garbage collection
    Performs out-of-place writes due to erase-before-write property
  Wear leveling
    To prolong SSD lifetime by evenly distributing P/E cycles
  Data refresh
    Resets transient errors by copying data to a new page(s)
  I/O scheduling
    To take full advantage of SSD internal parallelism

## Slide 20: Flash Translation Layer: Overview
SSD firmware (often referred to as SSD controller)
  Provides backward compatibility with traditional HDDs
  By hiding unique characteristics of NAND flash memory
Responsible for many important SSD-management tasks
  Address translation + garbage collection
    Performs out-of-place writes due to erase-before-write property
  Wear leveling
    To prolong SSD lifetime by evenly distributing P/E cycles
  Data refresh
    Resets transient errors by copying data to a new page(s)
  I/O scheduling
    To take full advantage of SSD internal parallelism

## Slide 21: Simple SSD Architecture
NAND Flash Chip (Single Plane)
Flash Translation Layer
Page
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Storage view at the operating-system level: A flat block device
LBA
Logical Block Address

## Slide 22: Simple SSD Architecture
NAND Flash Chip (Single Plane)
Flash Translation Layer
Page
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
PPA
Phygical Page Address
PBA
Phygical Block Address
LBA
Logical Block Address
Overprovisioning:
Physical capacity > Logical capaciy
For performance & lifetime

## Slide 23: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19

## Slide 24: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)

## Slide 25: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)

## Slide 26: Write Request Handling: Page Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A)
Note:
We are asumming that logical block size = physical page size
LB size = 4 KiB, PP size = 16 KiB

## Slide 27: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19

## Slide 28: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
Block0
Block1
Block2
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
Req (LBA: 4, Size: 12, DIR: W, B … M)

## Slide 29: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
PROG(PPA: 1, B)
PROG(PPA: 2, C)
PROG(PPA: 12, M)
…
12 page-program commands
Req (LBA: 4, Size: 12, DIR: W, B … M)

## Slide 30: Write Request Handling: Sequential Write
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Sequential (large) write
PROG(PPA: 1, B)
PROG(PPA: 2, C)
PROG(PPA: 12, M)
…
12 page-program commands
Req (LBA: 4, Size: 12, DIR: W, B … M)
Active block (or write-point) approach
  Keep only one block being written
  Due to the open-block problem
Program-sequence constraint
  Fixed program order within a block
  Due to cell-to-cell interference

## Slide 31: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Problem: LBA (or LPA) does not match PPA!

## Slide 32: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Problem: LBA (or LPA) does not match PPA!
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: ?)
Needs to maintain
Address-mapping information

## Slide 33: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: ?)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 34: Write Request Handling: Address Mapping
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 4, Size: 1, DIR: R)
READ (PPA: 1)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 35: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 36: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 37: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
READ (PPA: 13)
LPA | PPA
0 | 0
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 38: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
READ (PPA: 13)
LPA | PPA
0 | 13
… | …
4 | 1
5 | 2
… | …
Mapping Table
Invalid
Update Mapping

## Slide 39: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
READ (PPA: 14)
LPA | PPA
0 | 14
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 40: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
READ (PPA: 15)
LPA | PPA
0 | 15
… | …
4 | 1
5 | 2
… | …
Mapping Table

## Slide 41: Write Request Handling: Update
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
Req (LBA: 0, Size: 1, DIR: W, A’)
READ (PPA: 16)
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
Running
out of free pages

## Slide 42: Garbage Collection
Reclaims free pages by erasing invalid pages
  Erase unit: block
  If a victim block (to erase) has valid pages, all the valid pages need to be copied to other free pages
    Performance overhead: (tREAD + tPROG)×# of valid pages
    Lifetime overhead: additional writes  P/E-cycle increase
Greedy victim-selection policy: Erases the block with the largest number of invalid pages
  Needs to maintain # of invalid (or valid) pages for each block

## Slide 43: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | VIII
4 | VFFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)

## Slide 44: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | VIII
4 | VFFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)

## Slide 45: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
5 | 2
… | …
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status

## Slide 46: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 12
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping

## Slide 47: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping

## Slide 48: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
M
A’
A’
A’
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
Update Status
Update Mapping
Q: How FTL knows PPA 12 (data M) is mapped to LPA 15?
  Unless it maintains P2L mappings?
A: P2L mapping is stored in each physical page’s OOB (Out-of-Band) area

## Slide 49: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | IIII
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)

## Slide 50: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | FFFF
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)
Update Status

## Slide 51: Write Request Handling: Garbage Collection
NAND Flash Chip (Single Plane)
Flash Translation Layer
A
B
C
D
Block0
E
F
G
H
Block1
I
J
K
L
Block2
Block3
A’
M
Block4
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
A’ |  |  |  | B | C | D | E | F | G | H | I | J | K | L | M
Host
SSD
4
5
6
7
0
1
2
3
12
13
14
15
8
9
10
11
16
17
18
19
LPA | PPA
0 | 16
… | …
4 | 1
… | …
15 | 17
Mapping Table
PBA | Status
0 | IVVV
1 | VVVV
2 | VVVV
3 | FFFF
4 | VVFF
Status Table
F: free, V: valid, I: invalid
READ (PPA: 12)
PROG (PPA: 17, M)
BERS (PBA: 3)
Update Status
Note:
Block erasure (and status update) is done just before programming a new page to the block (i.e., lazy erase)
  Due to the open-block problem

## Slide 52: Performance Issues
Garbage collection significantly affects SSD performance
  High latency: Large block size of modern NAND flash memory
    Assume 1) a block contains 576 pages, 2) only 5% of the pages in the victim block are valid 3) tR = 100 us, tPROG = 700 us, tBERS = 5 ms
      # of pages to copy = 576×0.05 = 28.8  28 pages
      GC latency > 28×(tR + tPROG) + tBERS = 27,400 us
    Order(s) of magnitude larger latency than tR and tPROG
    Copy operations are the major contributor (rather than tBERS)
  If FTL performs GC in an atomic manner, it delays user requests for a significantly long time
    Long tail latency (performance fluctuation)
    Noisy neighbor: a read-dominant workload’s performance would be significantly affected when running with a write-intensive workload (+ performance fairness problem)

## Slide 53: Performance Issues: Mitigation
TRIM (UNMAP or discard) command
  Informs FTL of deletion/deallocation of a logical block
  Allows FTL to skip copy of obsolete (i.e., invalid) data
Background GC: Exploits SSD idle time
  Challenge: how to accurately predict SSD idle time
  Premature GC: copied pages could have been invalidated by the host system
Progressive GC: Divide GC process into subtasks
  e.g., copying 28 pages  (copying 1 page + servicing user request)×28
  Effective at decreasing tail latency

## Slide 54: Required Materials
Address Mapping
  Aayush Gupta, Yongjae Kim, and Bhuvan Urgaonkar, “DFTL: A Flash Translation Layer Employing Demand-based Selective Caching of Page-level Address Mappings,” In ASPLOS 2009.

## Slide 55: Recommend Materials
Cache read & Read-retry
  Jisung Park, Myungsuk Kim, Lois Orosa, Jihong Kim, and Onur Mutlu, “Reducing Solid-State Drive Read Latency by Optimizing Read-Retry,” In ASPLOS 2021.
Program & Erase Suspension
  Guanying Wu and Xunbin He, “Reducing SSD Read Latency via NAND Flash Program and Erase Suspension,” In USENIX FAST 2012.
  Shine Kim, Jonghyun Bae, Hakbeom Jand, Wenjing Jin, Jeonghun Gong, Seungyeon Lee, Tae Jun Ham, and Jae W. Lee, “Practical Erase Suspension for Modern Low-latency SSDs,” In USENIX ATC 2019.

## Slide 56: P&S Modern SSDs Advanced NAND Flash Commands & Address Translation
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Spring 2022
4 April 2022