## Slide 1: P&S Modern SSDs Research Session 1: Data Sanitization and Read-Retry in Modern NAND Flash-Based SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Spring 2022
15 July 2022

## Slide 2: Outline
NAND Flash Basics
Read-Retry in Modern NAND Flash-Based SSDs
Data Sanitization in Modern NAND Flash-Based SSDs

## Slide 3: NAND Flash-Based SSDs
A complicated embedded system
  Multiple cores, HW controllers, DRAM, and NAND flash chips
NAND Flash Chips
Persistent data store
LPDDR DRAM
Metadata store
SSD Controller
ARM Cores Running firmware
HW Flash Controllers Chip control, ECC
Samsung PM853T 960GB Enterprise SSD (from https://www.tweaktown.com/reviews/6695/samsung-pm853t-960gb-enterprise-ssd-review/index.html)
Unique characteristics
Erase-before-write
Limited endurance
High error rates
…

## Slide 4: Flash Cell
Stores data using its threshold voltage (VTH) level
  Dictated by the amount of electrons (i.e., charge) in the cell
  The more the electrons, the higher the VTH level
Flash Cell
Program:
Injects electrons
Erase:
Ejects electrons
Read:
Compares w/
reference level
1
0
1. Can change VTH (=charge) in a non-volatile manner
2. Encodes bit data with different VTH ranges

## Slide 5: Flash Cell Characteristics
Multi-leveling: A single flash cell can store multiple bits
Retention loss: A cell leaks electrons over time
Limited lifetime: A cell wears out after P/E cycling
11
01
00
10
2-Bit Multi-Level Cell (MLC)
1 year
1 year
11
01
00
10
11
01
00
10
11
01
00
10
00
Retention error!
1 year
@ 1K P/E cycles
1 year
@ 10K P/E cycles
11
01
00
10
11
01
00
10
00
Retention error!
11
01
00
10
1
0
Single-Level Cell (SLC)

## Slide 6: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
<100,000 cells
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
Long latency,
but high bandwidth
No overwrite of WLs
before erasing the block:
Erase-before-write
1
0
0
1
0
1
1
0

## Slide 7: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
⋯
Page (16 KiB)
Block (127 pages)
127
126
⋯
1
0
(16,384× 8 + α) cells

## Slide 8: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
Page (16 KiB)
Triple-Level Cell (TLC)
Block (127×3 pages)
4
3
2
1
0
⋯
381
380
379
378
⋯
Share the same cells (WL)
(16,384× 8 + α) cells

## Slide 9: Pipelined & Adaptive Read-Retry
The 26th International Conference on Architectural Support
for Programming Languages and Operating Systems
(ASPLOS’21)

## Slide 10: Problem: Long, Non-Deterministic Latency
NAND Flash-Based SSD
Read request (4 KiB)
Requested data
Expected latency: 100 µs
Actual latency: > 1 ms
Degrades the quality of service
of read-intensive, latency-sensitive applications

## Slide 11: Problem: Long, Non-Deterministic Latency
Requested data
Expected latency: 100 µs
Actual latency: > 1 ms
Flash-Translation Layer (FTL):
SSD Firmware
Flash Controller#1
NAND
Flash
Chip#1
NAND
Flash
Chip#2
⋯
⋯
Read Chip#2
Read CMD
NAND Flash-Based SSD
Retries
Internal Read-Retry Operations
Read request (4 KiB)

## Slide 12: Errors in NAND Flash Memory
NAND flash memory stores data by using cells’ VTH levels
Number of Cells
1
Erased State
0
Programmed
State
Cell’s VTH Level
Read–Reference Voltage VREF
<VTH Distribution of an SLC Page>
VREF
1
0
VREF
1
0

## Slide 13: Errors in NAND Flash Memory
Various sources shift and widen programmed VTH states
  Retention loss, program interference, read disturbance, etc.
Number of Cells
1
Erased State
0
Programmed
State
Cell’s VTH Level
Read–Reference Voltage VREF
<VTH Distribution of an SLC Page>
Retention loss
Interference
Errors

## Slide 14: Error-Correcting Codes (ECC)
Store redundant information (ECC parity)
  To detect and correct row bit errors
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Read Page 0

## Slide 15: Error-Correcting Codes (ECC)
Store redundant information (ECC parity)
  To detect and correct row bit errors
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Corrected data

## Slide 16: Errors in Modern NAND Flash Memory
High row bit-error rates (RBER) in MLC NAND flash memory
  Narrow margin b/w adjacent VTH states
# of cells
Erased (E)
0
Programmed
1
VREF
VTH
<VTH Distribution of an SLC Page>
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
VREF0
VREF1
VREF2
VREF3
VREF4
VREF5
VREF6
VTH Margin
VTH
<VTH Distribution of a TLC Page>

## Slide 17: Errors in Modern NAND Flash Memory
High row bit-error rates (RBER) in MLC NAND flash memory
  Narrow margin b/w adjacent VTH states
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
VREF0
VREF1
VREF2
VREF3
VREF4
VREF5
VREF6
VTH Margin
VTH
<VTH Distribution of a TLC Page>
Strong ECC: Corrects ~80 bit errors per 1-KiB data
Not Scalable: Area, power, latency, …
What if RBER > ECC Capability?

## Slide 18: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px State
P(x-1) State
…
P(x+1) State
V
REF(x-1)
V
REFx
Cell’s VTH Level
V
REF(x-2)
V
REF(x+1)
Erroneous cells

## Slide 19: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px State
P(x-1) State
…
P(x+1) State
V
REF(x-1)
V
REFx
V
REF(x-2)
V
REF(x+1)
V’
REF(x-2)
V’
REF(x-1)
V’
REFx
V’
REF(x+1)
Erroneous cells
Read-retry: Adjusting VREF values
Cell’s VTH Level
Read using properly-adjusted VREF values
Decreases # of raw bit errors
to be lower than the ECC capability

## Slide 20: Read-Retry: Performance Overhead
NERR = 32
< ECC capability CECC = 72
READ A
tREAD
tR: Page sensing
tDMA: Data transfer
tECC: ECC decoding

## Slide 21: Read-Retry: Performance Overhead
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
Read-retry increases the read latency
almost linearly with the number of retry steps

## Slide 22: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 23: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
In common cases, multiple (up to 25) retry steps occur

## Slide 24: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
In common cases, multiple (up to 25) retry steps occur
 Speculatively starts the next retry step
Speculative start

## Slide 25: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY’
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
= N×tR+tDMA+tECC
> ECC capability CECC = 72
tDMA
Removes tDMA & tECC
(~30% of each retry step) from the critical path
Latency
Reduction
Speculative start

## Slide 26: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 27: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×tR+tDMA+tECC
NERR = 118
RR2
> ECC capability CECC = 72
tDMA

## Slide 28: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
A large ECC margin
in the final retry step when read-retry succeeds
 Can we leverage this ECC (reliability) margin?

## Slide 29: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
Trading the large ECC margin to reduce tR
tR’ = α×tR
+ e1
+ eN-1
+ e2
+ eN

## Slide 30: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
Trading the large ECC margin to reduce tR
tR’ = α×tR
+ e1
+ eN-1
+ e2
+ eN
 Further reduction in the read-retry latency
= N×α×tR+tDMA+tECC
Latency
Reduction

## Slide 31: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
AR2 reduces tR in every retry step
+ e1
+ eN-1
+ e2
= N×α×tR+tDMA+tECC
Latency
Reduction
NERR = 23
> ECC capability CECC = 72
+ eN
tR’ = α×tR

## Slide 32: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
AR2 reduces tR in every retry step
+ e1
+ eN-1
+ e2
= N×α×tR+tDMA+tECC
Latency
Reduction
tR’ = α×tR
NERR = 23
> ECC capability CECC = 72
+ eN
ensuring NERR < CECC in the final retry step

## Slide 33: Real-Device Characterization
160 real 48-layer TLC NAND flash chips
Observation 1: A large ECC margin in the final retry step even under worst-case operating conditions
  At most 40 errors per KiB under 1–year retention time @ 2K program and erase (P/E) cycles
  Use of near-optimal VREF in the final retry step
Observation 2: A large reliability margin incorporated in read-timing parameters
  25% tR reduction  At most 23 additional errors
  Worst-case-based design due to process variations
AR2 can easily work in commodity
NAND flash chips w/ at least 25% tR reduction

## Slide 34: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
READ A
READ A
Data A
Fail
tDMA
tECC
tR
ECC fail

## Slide 35: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
Fail
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶

## Slide 36: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶
Read-retry w/ best tR + speculative start
❷
Best tR
⋯
ECC success
Page A

## Slide 37: P&AR2: Design
SSD Firmware (FTL)
PEC | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶
Read-retry w/ best tR + speculative start
❷
Best tR
⋯
ECC success
Page A
Key Takeaway
Strong ECC: to avoid read-retry as much as possible
 Can provide high reliability margin
when read-retry occurs
 Can be used to reduce the read-retry latency

## Slide 38: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 39: Evaluation Results
Simulation using MQSim [Tavakkol+, FAST18] and 12 real-world workloads
Our proposal improves SSD response time by
    Up to 51% (35% on average) compared to a high-end SSD w/o read-retry mitigation
    Up to 32% (17% on average) compared to a state-of-the-art read-retry mitigation technique [Shim+, MICRO19]

## Slide 40: Outline
NAND Flash Basics
Read-Retry in Modern NAND Flash-Based SSDs
Data Sanitization in Modern NAND Flash-Based SSDs

## Slide 41: Access Control-Based Data Sanitization
The 25th International Conference on Architectural Support
for Programming Languages and Operating Systems
(ASPLOS’20)

## Slide 42: Data-Remanence Problem in SSDs
File System
0
1
2
3
4
5
6
7
8
A0
A1
A2
…
A.txt
NAND Flash-Based SSD
CTRL
DRAM
NAND
NAND
NAND
Flash
NAND
Flash
A0
0
A1
1
A2
2
Page
3
Blk#0
4
5
6
7
Blk#1
8
9
10
11
Blk#2
12
13
14
15
Blk#3
Deleted data can remain in SSDs for indefinite time

## Slide 43: Data-Remanence Problem in SSDs
File System
0
1
2
3
4
5
6
7
8
A0
A2
…
A.txt
NAND Flash-Based SSD
CTRL
DRAM
NAND
NAND
A0
0
A1
1
A2
2
Page
3
Blk#0
4
5
6
7
Blk#1
8
9
10
11
Blk#2
12
13
14
15
Blk#3
A1’
Update
A1
A1’
No overwrite
 Out-of-place update
Deleted data can remain in SSDs for indefinite time
NAND
Flash
NAND
Flash

## Slide 44: Data-Remanence Problem in SSDs
File System
0
1
2
3
4
5
6
7
8
A0
A2
B0
B1
B2
…
A.txt
NAND Flash-Based SSD
CTRL
DRAM
NAND
NAND
A0
0
A1
1
A2
2
Page
3
Blk#0
B0
4
B1
5
B2
6
7
Blk#1
8
9
10
11
Blk#2
12
13
14
15
Blk#3
A1’
A1
A1’
B.png
Deleted data can remain in SSDs for indefinite time
NAND
Flash
NAND
Flash

## Slide 45: Data-Remanence Problem in SSDs
File System
0
1
2
3
4
5
6
7
8
A0
A2
B0
B1
B2
…
A.txt
NAND Flash-Based SSD
CTRL
DRAM
NAND
NAND
A0
0
A1
1
A2
2
Page
3
Blk#0
B0
4
B1
5
B2
6
7
Blk#1
8
9
10
11
Blk#2
12
13
14
15
Blk#3
A1’
A1
A1’
B.png
Delete
B0
B1
B2
Q: When is a page erased?
A: Only in garbage collection
= when running out of free pages
Deleted data can remain in SSDs for indefinite time
NAND
Flash
NAND
Flash

## Slide 46: Data-Recovery Attack
NAND Flash-Based SSD
NAND Flash Chip
File System
0
1
2
3
4
5
6
7
8
A0
A2
B0
B1
B2
…
A.txt
CTRL
DRAM
NAND
NAND
A0
0
A1
1
A2
2
Page
3
Blk#0
B0
4
B1
5
B2
6
7
Blk#1
8
9
10
11
Blk#2
12
13
14
15
Blk#3
A1’
A1
A1’
B.png
B0
B1
B2
ADVERSARY
1. Detach the SSD
2. Detach the chip
3. Direct access to the chip
A0
A1
A2
B1
4. Run forensic tools
A.txt
B.png
System requirement: Obsolete data must be inaccessible
NAND
Flash
NAND
Flash

## Slide 47: Existing Solutions
Why not immediately erase an invalid page?
  Erase unit: a block (> 1,000 pages)
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
N Pages
(>1,000)
Target Page
⋯
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Free Block
Copy NValid Pages
⋯
NValid
tCOPY=NValid×(tREAD+tPROG)
Wasted

## Slide 48: Existing Solutions
Why not immediately erase an invalid page?
  Erase unit: a block (> 1,000 pages)
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
N Pages
(>1,000)
Target Page
⋯
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Free Block
Copy NValid Pages
⋯
NValid
tCOPY=NValid×(tREAD+tPROG)
Wasted
Immediate block erasure causes
prohibitive performance and lifetime overhead

## Slide 49: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Reprograms all the flash cells storing an invalid page
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
0
1
0
1
⋯
1
0
0
1
WL1
Erased (1)
Programmed (0)

## Slide 50: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Reprograms all the flash cells storing an invalid page
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
0
0
0
0
⋯
0
0
0
0
WL1
Scrubbed
Scrubbing: Reprogram the WL (to all ‘0’s)
Overwriting is infeasible usually,
except when the data is all ‘0’s
Erased (1)
Programmed (0)
Destroys the page data w/o block erasure
Problem solved?

## Slide 51: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem1: MLC NAND flash stores multiple pages in a WL
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL0
Page 0
0
1
0
0
1
1
0
1
⋯
Page 1
0
1
0
1
1
0
0
1
⋯
Page 2
1
1
0
0
0
0
1
0
⋯

## Slide 52: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem1: MLC NAND flash stores multiple pages in a WL
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL0
Page 0
1
1
1
1
1
1
1
1
⋯
Page 1
0
0
0
0
0
0
0
0
⋯
Page 2
1
1
1
1
1
1
1
1
⋯
Scrubbing in MLC NAND flash memory  Destroys other valid pages  Copy overheads

## Slide 53: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem 1: MLC NAND flash stores multiple pages in a WL
  Problem 2: Program interference
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL0
Page 3
0
1
0
0
1
1
0
1
⋯
Page 4
0
1
0
1
1
0
0
1
⋯
Page 5
1
1
0
0
0
0
1
0
⋯
⋯
WL1

## Slide 54: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem 1: MLC NAND flash stores multiple pages in a WL
  Problem 2: Program interference
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL1
Page 3
0
1
0
0
1
1
0
1
⋯
Page 4
0
1
0
1
1
0
0
1
⋯
Page 5
1
1
0
0
0
0
1
0
⋯
⋯
WL0
Program interference (slight program)

## Slide 55: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem 1: MLC NAND flash stores multiple pages in a WL
  Problem 2: Program interference
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL1
Page 3
0
1
0
0
1
0
0
1
⋯
Page 4
0
1
0
1
1
0
0
0
⋯
Page 5
1
0
0
0
0
0
1
0
⋯
⋯
WL0
Program interference (slight program)

## Slide 56: Existing Solutions
Scrubbing [Wei+, FAST’11]
  Problem 1: MLC NAND flash stores multiple pages in a WL
  Problem 2: Program interference
⋯
Valid
Invalid
Free
Target Block
3
4
5
⋯
0
1
2
N – 3
N – 2
N – 1
Target Page
Scrubbed
⋯
WL1
Page 3
0
1
0
0
1
0
0
1
⋯
Page 4
0
1
0
1
1
0
0
0
⋯
Page 5
1
0
0
0
0
0
1
0
⋯
⋯
WL0
Program interference (slight program)
Existing solutions incur
performance, lifetime, and reliability problems
in modern NAND flash memory

## Slide 57: Evanesco: Outline
Data Remanace in NAND Flash-Based SSDs
Evanesco: Access Control–Based Sanitization
Evaluation Results

## Slide 58: Our Solution: Evanesco
Allows a NAND flash chip to be aware of data validity
  On-chip access control to avoid access to invalid data
  Low overhead: No copy operations
  High reliability: No program interference
Two new NAND commands: pageLock and blockLock
read(2)
00…0
(all-zero data)
pLock(3)
bLock(0)
0
1
2
3
Block#0
4
5
6
7
Block#1
B0’
A0
A1
A2
NAND
Flash
B0
B0
E
E
E
E
E
E
E
E
D
D
D
D
Flags#1
Flags#0
EVANESCO!
B0
A0
A1
A2
A0
A1
A2

## Slide 59: Evanesco: Requirements
Keep access-permission flags in a non-volatile manner
Access-control logic inside a NAND flash chip
Minimal area overhead  High chip densitity is paramount
read(2)
00…0
(all-zero data)
pLock(3)
bLock(0)
0
1
2
3
Block#0
4
5
6
7
Block#1
B0’
A0
A1
A2
B0
B0
E
E
E
E
E
E
E
E
D
D
D
D
Flags#1
Flags#0
EVANESCO!
B0
A0
A1
A2
A0
A1
A2
NAND
Flash

## Slide 60: pLock: Page-Level Data Sanitization
On-chip access-permission flags: Spare cells in each WL
⋯
WL0
Page Data Area
⋯
Spare Area

## Slide 61: pLock: Page-Level Data Sanitization
On-chip access-permission flags: Spare cells in each WL
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
MSB Page
CSB Page
LSB Page
Erased = Enabled
Programmed = Disabled

## Slide 62: pLock: Page-Level Data Sanitization
On-chip access-permission flags: Spare cells in each WL
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
MSB Page
CSB Page
LSB Page
Erased = Enabled
Programmed = Disabled
pLock(page0)

## Slide 63: pLock: Page-Level Data Sanitization
On-chip access-permission flags: Spare cells in each WL
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
Erased = Enabled
Programmed = Disabled
pLock(page0)
⋯
WL1
M
C
L
⋯
No program of data cells little interference
SLC  Robust to the interference
Interference b/w flag cells

## Slide 64: pLock: Page-Level Data Sanitization
On-chip access-permission flags: Spare cells in each WL
On-chip access control logic: Small changes to data path
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
Erased = Enabled
Programmed = Disabled
⋯
WL1
M
C
L
⋯

## Slide 65: pLock: Page-Level Data Sanitization
On-chip access-permision flags: Spare cells in each WL
On-chip access control logic: Small changes to data path
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
Erased = Enabled
Programmed = Disabled
⋯
WL1
M
C
L
⋯
⋯
WLN-1
M
C
L
⋯
Page Buffer
Data Out
Bitlines (BLs)
0
1
0
0
1
1
0
1
0
1
1
READ(page0)

## Slide 66: pLock: Page-Level Data Sanitization
On-chip access-permision flags: Spare cells in each WL
On-chip access control logic: Small changes to data path`
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Page Data Area
M
C
L
⋯
Spare Area
Erased = Enabled
Programmed = Disabled
⋯
WL1
M
C
L
⋯
⋯
WLN-1
M
C
L
⋯
Page Buffer
Data Out
Bitlines (BLs)
MUX
Bridge
Transistor
0
1
0
0
1
1
0
1
0
1
1
0 (disconnect)
READ(page0)
00…0

## Slide 67: Real-Device Characterization
Using 160 real 48-layer TLC NAND flash chips
No reliability degradation for stored data
tPLOCK = 100 µs, tBLOCK = 300 µs
Evanesco: No copy operation, no reliability issues w/ minimal changes to NAND flash chip designs
But the performance overhead is not negligible

## Slide 68: SecureSSD: System-Level Optimization
To minimize the performance overhead of data sanitization
  Issues pLock and bLock commands depending on the status of the target block
⋮
Block#m
Multiple invalid pages +
no valid pages in the block
⋮
Block#k
Valid
Invalid
Delete A
Trim (discard) LPAs
bLock
pLock
File System
A.png
B.doc
Application
SecureSSD
Evanesco-Aware FTL
L2P
Mapping
Table
Page
Status
Table
Flash Chip
Flash Chip
NAND Flash
A.png
B.doc
pLock
bLock
⋯
A.png
A.png
Lock
Manager

## Slide 69: SecureSSD: System-Level Optimization
To minimize the performance overhead of data sanitization
  Issues pLock and bLock commands depending on the status of the target block
  Cross-layer interactions for selective data sanitization
Delete B
Trim (discard) LPAs
File System
A.png
B.doc
Application
SecureSSD
Evanesco-Aware FTL
L2P
Mapping
Table
Page
Status
Table
Flash Chip
Flash Chip
NAND Flash
A.png
B.doc
⋯
A.png
A.png
Lock
Manager
fd = open(“B.doc”, O_CREATE|O_INSEC);
// create security-insensitive file B.doc
bio->bi_of =| REQ_OP_INSEC_WRITE;
// set low security requirement
ExtendedPG Status
Table
Set page status to INSECURE
B.doc
Invalidation w/o pLock or bLock
B.doc

## Slide 70: Evanesco: Outline
Data Remanace in NAND Flash-Based SSDs
Evanesco: Access Control–Based Sanitization
Evaluation Results

## Slide 71: Results: Performance
Normalized IOPS
Chart: 
| MailServer | DBServer | FileServer | Mobile
erSSD | 0.0040514 | 0.0037037 | 0.0006891 | 0.034454
scrSSD | 0.44049 | 0.20679 | 0.20397 | 0.56471
secSSD | 0.9803 | 0.89198 | 0.96164 | 0.95462
erSSD
scrSSD
SecureSSD
0.98
0.96
0.95
0.89
0.004
0.003
0.0007
0.034
0.44
0.21
0.2
0.56
Evanesco significantly reduces performance overhead of data sanitization
(11% slowdown at most)

## Slide 72: Results: Lifetime
Normalized WAF
Chart: 
| MailServer | DBServer | FileServer | Mobile
erSSD | 184.9203 | 285.3769 | 254.4159 | 320.159
scrSSD | 2.9415 | 3.3282 | 4.4166 | 1.4928
secSSD | 0.99777 | 1.0006 | 1.0045 | 1.0066
erSSD
scrSSD
SecureSSD
Write Amplification Factor
184.9
285.3
245.4
320.2
2.9
3.3
4.4
1.5
No additional copy for data sanitization
 No lifetime overhead

## Slide 73: Summary of Contribution
Problem1: Long, non-deterministic SSD read latency
  Due to essential reliability management (read-retry)
  Performance degradation of data-intensive applications
Our solution: Pipelined & adaptive read-retry
  Leveraging device characteristics and ECC margin
  Reducing read-retry latency  easy to combine with other optimizations
Problem2: Data remanence in NAND flash-based SSDs
  Obsolete data remains intact in SSDs for an indefinite time
  Physical data destrubtion: prohibitive performance overheads
Our solution: Access control-based data sanitization
  Avoids transfer of obsolete data from NAND flash chips
  Minimal performance and reliability overheads

## Slide 74: P&S Modern SSDs Research Session 1: Data Sanitization and Read-Retry in Modern NAND Flash-Based SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Spring 2022
15 July 2022